***Scenario 3-1 Configurations

Scenario 3-1 Switch-A Configuration

hostname Switch-A

!

vtp domain LANPS

vtp mode server

vtp password cisco

vtp version 2

!

vlan 2

name Sales

vlan 3

name Marketing

vlan 4

name Engineering

vlan 5

name Management

vlan 10

name Native

Scenario 3-1 Switch-B Configuration

set system name Switch-B

!

set vtp v2 enable

set vtp mode client

set vtp passwd cisco

set vtp domain LANPS

***Scenario 3-2 Configurations

Scenario 3-2 Switch-A Configuration

hostname Switch-A

!

vtp domain LANPS

vtp mode server

vtp password cisco

vtp version 2

!

vlan 2

name Sales

vlan 3

name Marketing

vlan 4

name Engineering

vlan 5

name Management

vlan 10

name Native

!

interface fastEthernet0/1

switchport trunk encapsulation dot1q

switchport mode dynamic desirable

switchport trunk native vlan 10

switchport trunk allowed vlan 2-5,10,1002-1005

!

interface fastEthernet0/3

switchport access vlan 3

!

interface fastEthernet0/4

switchport access vlan 4

!

interface fastEthernet0/5

switchport access vlan 2

!

interface vlan 5

ip address 192.168.5.2 255.255.255.0

Scenario 3-2 Switch-B Configuration

set system name Switch-B

!

set vtp v2 enable

set vtp mode client

set vtp passwd cisco

set vtp domain LANPS

!

set vlan 2 2/3

set vlan 3 2/4

set vlan 10 2/1

!

set trunk 2/1 desirable dot1q

clear trunk 2/1 1-1005,1025-4094

set trunk 2/1 2-5,10

!

set interface sc0 5 192.168.5.3 255.255.255.0

***Scenario 3-3 Configurations

Scenario 3-3 Switch-A Configuration

hostname Switch-A

!

vtp domain LANPS

vtp mode server

vtp password cisco

vtp version 2

vtp pruning

!

vlan 2

name Sales

vlan 3

name Marketing

vlan 4

name Engineering

vlan 5

name Management

vlan 10

name Native

!

interface fastEthernet0/1

switchport trunk encapsulation dot1q

switchport mode dynamic desirable

switchport trunk native vlan 10

switchport trunk allowed vlan 2-5,10,1002-1005

switchport trunk pruning vlan 4

!

interface fastEthernet0/3

switchport access vlan 3

!

interface fastEthernet0/4

switchport access vlan 4

!

interface fastEthernet0/5

switchport access vlan 2

!

interface vlan 5

ip address 192.168.5.2 255.255.255.0

Scenario 3-3 Switch-B Configuration

set system name Switch-B

!

set vtp v2 enable

set vtp mode client

set vtp passwd cisco

set vtp domain LANPS

clear vtp pruneeligible 2-1005

set vtp pruneeligible 4

!

set vlan 2 2/3

set vlan 3 2/4

set vlan 10 2/1

!

set trunk 2/1 desirable dot1q

clear trunk 2/1 1-1005,1025-4094

set trunk 2/1 2-5,10

!

set interface sc0 5 192.168.5.3 255.255.255.0

***Scenario 3-4 Configurations

Scenario 3-4 Switch-A Configuration

hostname Switch-A

!

vtp domain LANPS

vtp mode server

vtp password cisco

vtp version 2

vtp pruning

!

vlan 2

name Sales

vlan 3

name Marketing

vlan 4

name Engineering

vlan 5

name Management

vlan 10

name Native

!

port-channel load-balance dst-mac

!

interface PortChannel 1

switchport trunk encapsulation dot1q

switchport mode dynamic desirable

switchport trunk native vlan 10

switchport trunk allowed vlan 2-5,10,1002-1005

switchport trunk pruning vlan 4

!

interface range fastEthernet0/1 - 2

speed 100

duplex full

switchport trunk encapsulation dot1q

switchport mode dynamic desirable

switchport trunk native vlan 10

switchport trunk allowed vlan 2-5,10,1002-1005

switchport trunk pruning vlan 4

channel-group 1 mode desirable

!

interface fastEthernet0/3

switchport access vlan 3

!

interface fastEthernet0/4

switchport access vlan 4

!

interface fastEthernet0/5

switchport access vlan 2

!

interface vlan 5

ip address 192.168.5.2 255.255.255.0

Scenario 3-4 Switch-B Configuration

set system name Switch-B

!

set vtp v2 enable

set vtp mode client

set vtp passwd cisco

set vtp domain LANPS

clear vtp pruneeligible 2-1005

set vtp pruneeligible 4

!

set vlan 2 2/3

set vlan 3 2/4

set vlan 10 2/1

!

set trunk 2/1 desirable dot1q

clear trunk 2/1 1-1005,1025-4094

set trunk 2/1 2-5,10

set trunk 2/2 desirable dot1q

clear trunk 2/2 1-1005,1025-4094

set trunk 2/2 2-5,10

!

set interface sc0 5 192.168.5.3 255.255.255.0

!

set port speed 2/1-2 100

set port duplex 2/1-2 full

set port channel 2/1-2 desirable

set port channel 2/1-2 100

set port channel all distribution session source