CCNP BCRAN Exam Certification Guide, Second Ed.

(CCNP Self-Study, 642-821)

ISBN: 1-58720-084-8

Cisco Press

# Errata

The following questions on the accompanying CD have wrong answers:

44, 140, 154, 209

Page 41 - Section under ‘Server-to-Server’

‘Sever-to-server VPNs’ should be spelled ‘Server-to-server VPNs’

Page 132 – Regarding Example 6-2, the fifth & eighth lines of the configuration should read,

respectively:

Server (config – if) #ip address 10.1.1.2 255.255.255.0

Server (config – if) #dialer map ip 10.1.1.1 name Client 6553434

Page 133, first paragraph, last sentence

“The value is configurable using the dialer hold-queue command detailed later in this chapter” is incorrect twice.

The command “dialer hold-queue” is the size of the buffer for packets waiting to go out over the ISDN interface, and the command is not discussed further in this chapter for sure.

Page 165 – The second sentence of the paragraph under the heading ‘Caller ID Screening’

should read, “The isdn caller command is used for this purpose.”

Page 182, Example 8-3

“dialer load threshold 50 either”

Should read “dialer load-threshold 50 either”

Page 301, second to last paragraph, second sentence

“The parameters are more related to BECN response to network congestion.”

Should read “The parameters are more related to BECN response than to 			network congestion”

Page 374, Example 16-1

“access-list 1 permit 10.0.0.1 0.0.0.255”

Should read “access-list 1 permit 10.0.0.0 0.255.255.255”

Page 440, the second to last line

“R1(config-iskamp)#”

Should read “R1(config-isakmp)#”

Page 470 – The Answer to question #6 should be:

interface BRI0

dialer pool-member 24

!

interface BRI1

dialer pool-member 24

!

interface BRI2

dialer pool-member 24

!

interface Dialer24

dialer pool 24

Page 482 – The Answer to question #7 should be: 780.