Implementing Cisco Unified Communications Voice over IP and QoS (CVoice)

Foundation Learning Guide

First Edition

Copyright © 2011 Cisco Systems, Inc.

ISBN-10: 1-58720-419-3
ISBN-13:  978-1-58720-419-7

Warning and Disclaimer

Every effort has been made to make this book as complete and as accurate as possible, but no warranty or fitness is implied. The information provided is on an "as is" basis. The author and the publisher shall have neither liability nor responsibility to any person or entity with respect to any loss or damages arising from the information contained in this book or from the use of the CD or programs accompanying it.

When reviewing corrections, always check the print number of your book. Corrections are made to printed books with each subsequent printing.

First Printing: May 2011

Corrections for May 14, 2013

| Pg | Error | Correction |
| --- | --- | --- |
| 451 | Chapter 5, Figure 5-21, first command for San Jose Reads: dial-peer voice 4000 pots destination-pattern 7135554… port 0/1:23 | Should read: dial-peer voice 4000 pots destination-pattern 7135554… forward-digits all port 0/1:23 |

| 451 | Chapter 5, First bullet point Reads: Router (config)#num-exp 4… 7135554… Router(config)#dial-peer voice 4000 pots Router(config-dial-peer)#destination-pattern 7135554… Router(config-dial-peer)#port 0/1:23 | Should read: Router(config)#num-exp 4… 7135554… Router(config)#dial-peer voice 4000 pots Router(config-dial-peer)#destination-pattern 7135554… Router(config-dial-peer)#forward-digits all Router(config-dial-peer)#port 0/1:23 |
| --- | --- | --- |

Corrections for April 5, 2013

| Pg | Error | Correction |
| --- | --- | --- |
| 102 | Chapter 1, Example 1-13, Third Config down Reads: Router1(config–controller)#linecoding hdb3 | Should read: Router1(config–controller)#linecode hdb3 |
| 102 | Chapter 1, Example 1-14, Third Config down Reads: Router2(config–controller)#linecoding ami | Should read: Router2(config–controller)#linecode ami |

Corrections for December 17, 2012

| Pg | Error | Correction |
| --- | --- | --- |
| 522 | Chapter 6, Table 6-2, Second section, second bullet under column titled Purpose Reads: other-gatekeeper-name: Name of remote gatekeeper’s domain. | Should read: other-domain-name: Name of remote gatekeeper’s domain |
| 533 | Chapter 6, Example 6-9, bottom command Reads: Router (config-dial-peer) #session target ras | Should read: Router (config-dial-peer) port 0/0/0:23 |
| 614 | Chapter 8, Example 8-1, last command Reads: access-list 100 permit tcp any any It 1024 | Should read: access-list 100 permit tcp any any It 1024 access-list 100 permit tcp any It 1024 any |
| 620 | Chapter 8, Example 8-5, First line, Reads: Router#show running-config | Should read: Switch#show running-config |
| 654 | Chapter 8, Figure 8-33, bottom line of the configuration box Reads: service out cust-policy | Should read: service-policy out shape-all |
| 672 | Chapter 8, First sentence under Monitoring Cisco AutoQoS for the Enterprise: Phase 1 Reads: The auto discovery qos command displays the results of the discovery phase. | Should read: The show auto discovery qos command displays the results of the discovery phase. |

Corrections for September 21, 2012

| Pg | Error | Correction |
| --- | --- | --- |
| 289 | Chapter 2, Figure 2-74, bottom line of first box Fax rate 4800 | Delete this bottom line |
| 452 | Chapter 5, Second Bullet, Last Sentence in paragraph Reads: Use the prefix command to send the prefix numbers 2815553 before forwarding the three wildcard-matched digits. | Should read: Use the prefix command to send the prefix numbers 12815553 before forwarding the three wildcard-matched digits. |
| 468 | Chapter 5, Last Bullet, Austin, First Sub-Bullet Reads: DID range 312 555-2XXX | Should read: DID range 512 555-2XXX |
| 473 | Chapter 5, Step 1, Fourth Sentence Reads: Dial peer 8011 is matched because it has the best preference, and the translation-profile outgoing intersite–out command is applied because this is an outbound call. | Should read: Dial peer 8010 is matched because it has the best preference, and the translation-profile outgoing intersite–out command is applied because this is an outbound call. |
| 477 | Chapter 5, Example 5-36, Fourth Line Down Reads: Rule 1 /^2/ /13125552/ | Should read: Rule 1 /^2/ /15125552/ |

Corrections for August 8, 2012

| Pg | Error | Correction |
| --- | --- | --- |
| 229 | Chapter 2, first syntax under first bullet point Reads: Router(config-voi-serv)#session transport {system ¦ tcp tls ¦ udp} | Should read: Router(config-voi-serv)#session transport { tcp tls ¦ udp} |
| 231 | Chapter 2, Figure 2-51, third line down Reads: session transport top | Should read: session transport tcp |
| 232 | Chapter 2, Example 2-5, last line Reads: session transport top | Should read: session transport tcp |
| 507 | Chapter 6, Figure 6-5, second arrow down labeled: RRQ Keepalive | Should be: Arrow should be going up: RRQ Keepalive |

Corrections for July 12, 2012

| Pg | Error | Correction |
| --- | --- | --- |
| 134 | Chapter 1, First Sentence Reads: The compute the total call bandwidth, the additional Layer 2 header must be considered, using the following formula: BW_per_call= (Voice_payload + L3+_overhead + L2_overhead) * Packet_ration)* 8 bits/byte | Should read: The compute the total call bandwidth, the additional Layer 2 header must be considered, using the following formula: BW_per_call= (Voice_payload + L3_overhead + L2_overhead) * Packet_ration)* 8 bits/byte |
| 141 | Chapter 1, Packet voice DSP Module Conferencing, first sentence Reads: PVDM2 modules offer more flexibility in resource sharing than the PVDM2 modules. | Should read: PVDM3 modules offer more flexibility in resource sharing than the PVDM2 modules. |
| 145 | Chapter 1, Secure, last sentence Reads: This setting supports the lowest number of selected low- and medium-complexity codecs (G.711 a-law and mu-law, G.729, and G.729A) per DSP. | Should read: This setting supports the lowest number of selected low- and medium-complexity codecs (G.711 a-law, G.711 mu-law, and G.729A) per DSP. |

Corrections for June 25, 2012

| Pg | Error | Correction |
| --- | --- | --- |
| 113 | Chapter 1, Example 1-18, add to bottom of example Add: Router(config-if)#no shutdown | Add: Router(config-if)#no shutdown |
| 115 | Chapter 1, Example 1-18, add after first line in example Add: Router1#configure terminal | Add: Router1#configure terminal |

Corrections for May 24, 2012

| Pg | Error | Correction |
| --- | --- | --- |
| 56 | Chapter 1, Step 4, first sentence Reads: R2 receives the called number (42001), matches the outbound dial peer 1, and forwards the called number (2001) in a single call setup message over the outgoing digital trunk, to R3. | Should read: R2 receives the called number (42001), matches the outbound dial peer 2, and forwards the called number (2001) in a single call setup message over the outgoing digital trunk, to R3. |

Corrections for March 26, 2012

| Pg | Error | Correction |
| --- | --- | --- |
| 648 | Figure 8-29, diamonds in middle of flow chart Reads: B < TP B < TC | Should be: B > TP B > TC |

Corrections for August 25, 2011

| Pg | Error | Correction |
| --- | --- | --- |
| 53 | Chapter 1, Figure 1-43, Step 9 in diagram Reads: Step 9. dial-peer voice 1 pots destination-pattern 2004 port 1/0/1. | Should read: Step 9. dial-peer voice 1 pots destination-pattern 2001 port 1/0/1. |

This errata sheet is intended to provide updated technical information. Spelling and grammar misprints are updated during the reprint process, but are not listed on this errata sheet.