***Scenario 9-1 Configurations

Scenario 9-1 XYZSW1 Configuration

hostname XYZSW1

!

no ip domain-lookup

!

enable secret cisco

!

mls qos

mls qos aggregate-police UNTRUSTED 1000000 64000 exceed-action drop

mls qos map cos-dscp 0 8 16 24 32 46 48 56

!

policy-map HOSTX

class-map VOIP access-group name VOIP

set ip dscp 46

class-map VOIP-CONTROL access-group name VOIP-CONTROL

set ip dscp 26

class-map BUSINESS access-group name BUSINESS

set ip dscp 28

class-map WEB access-group name WEB

set ip dscp 8

police 128000 8000

exceed-action drop

!

policy-map UNTRUSTED

class-map VOICE access-group 100

set ip dscp 46

police aggregate UNTRUSTED

!
interface GigabitEthernet0/1

description TRUNK TO XYZSW2

no shutdown

speed 100

duplex full

switchport trunk encapsulation dot1q

switchport mode trunk

mls qos trust dscp

wrr-queue cos-map 1 0 1 2

wrr-queue cos-map 2 3 4

wrr-queue cos-map 3 6 7

wrr-queue cos-map 4 5

wrr-queue bandwidth 10 40 50 0

wrr-queue random-detect max-threshold 2 60 80

wrr-queue dscp-map 1 28

wrr-queue dscp-map 2 26

priority-queue out

!

interface GigabitEthernet0/2

description TRUNK TO XYZSW3

no shutdown

speed 100

duplex full

switchport trunk encapsulation dot1q

switchport mode trunk

mls qos trust cos

wrr-queue cos-map 1 0 1 2

wrr-queue cos-map 2 3 4

wrr-queue cos-map 3 6 7

wrr-queue cos-map 4 5

wrr-queue bandwidth 10 40 50 0

wrr-queue random-detect max-threshold 2 60 80

wrr-queue dscp-map 1 28

wrr-queue dscp-map 2 26

priority-queue out

!

interface GigabitEthernet0/3

no shutdown

speed 100

duplex full

switchport mode access

service-policy input HOSTX

!

interface GigabitEthernet0/4

description TRUNK TO UNTRUSTED NETWORK

no shutdown

speed 100

duplex full

switchport trunk encapsulation dot1q

switchport mode trunk

service-policy input UNTRUSTED

wrr-queue cos-map 1 0 1 2

wrr-queue cos-map 2 3 4

wrr-queue cos-map 3 6 7

wrr-queue cos-map 4 5

wrr-queue bandwidth 10 40 50 0

wrr-queue random-detect max-threshold 2 60 80

wrr-queue dscp-map 1 28

wrr-queue dscp-map 2 26

priority-queue out

!

interface vlan 1

no shutdown

ip address 192.168.1.1 255.255.255.0

!

ip default-gateway 192.168.1.5

!

ip access-list extended VOIP

remark THIS ACL DEFINES VOIP TRAFFIC

permit udp any range 16384 32767 any range 16384 32767

ip access-list extended VOIP-CONTROl

remark THIS ACL DEFINES VOIP CONTROL TRAFFIC

permit tcp any any eq 1720

permit tcp any any range 11000 11999

permit tcp any any eq 2000

ip access-list extended WEB

remark THIS ACL DEFINES DOWNLOADED HTTP CONTENT FROM HOSTX

permit tcp any eq www any

ip access-list extended BUSINESS

remark THIS ACL DEFINES BUSINESS TRAFFIC SENT FROM HOSTX

permit tcp any any eq 10000

!

line vty 0 4

password cisco

Scenario 9-1 XYZSW2 Configuration

set system name XYZSW2

!

set interface sc0 192.168.1.2 255.255.255.0

set ip route default 192.168.1.5

!

set port speed 2/1-2 100

set port speed 2/3 10

set port duplex 2/1-2 full

set port duplex 2/3 half

set port qos 2/1 trust trust-dscp

set port qos 2/2 trust trust-cos

set port qos 2/3 trust untrusted

!

set trunk 2/1 on dot1q

set trunk 2/2 on dot1q

!

set qos enable

set qos cos-dscp-map 0 8 16 24 32 46 48 56

set qos map 2q2t tx 1 1 0,1,2

set qos map 2q2t tx 1 2 3,4

set qos map 2q2t tx 2 1 6,7

set qos map 2q2t tx 2 2 5

set qos wrr 2q2t 12 48

set qos drop-threshold 2q2t tx queue 2 60 80

!

set qos acl ip XYZR1 dscp 46 udp any range 16384 32767 any range 16384 32767

set qos acl ip XYZR1 dscp 26 tcp any any eq 1720

set qos acl ip XYZR1 dscp 26 tcp any any range 11000 11999

set qos acl ip XYZR1 dscp 26 tcp any any eq 2000

set qos acl ip XYZR1 dscp 28 tcp any any eq 10000

set qos acl ip XYZR1 dscp 8 any

set qos acl map XYZR1 2/3

!

commit qos acl XYZR1

Scenario 9-1 XYZSW3 Configuration

hostname XYZSW3

!

no ip domain-lookup

!

enable secret cisco

!

interface fastEthernet0/1

description TRUNK TO XYZSW1

no shutdown

speed 100

duplex full

switchport trunk encapsulation dot1q

switchport mode trunk

!

interface fastEthernet0/2

description PHONE X

no shutdown

speed auto

duplex auto

switchport mode access

switchport voice vlan dot1p

switchport priority extend cos 1

power inline auto

!

interface fastEthernet0/3

description TRUNK TO HOST Z

no shutdown

speed 100

duplex full

switchport trunk encapsulation dot1q

switchport mode trunk

switchport priority default 0

switchport priority override

!

interface vlan 1

no shutdown

ip address 192.168.1.3 255.255.255.0

!

ip default-gateway 192.168.1.5

!

line vty 0 4

password cisco

Scenario 9-1 XYZSW4 Configuration

set system name XYZSW4

!

set interface sc0 192.168.1.4 255.255.255.0

set ip route default 192.168.1.5

!

set port speed 2/1 100

set port speed 2/2 auto

set port speed 2/3 100

set port duplex 2/1 full

set port duplex 2/2 auto

set port duplex 2/3 full

!

set trunk 2/1 on dot1q

!

set qos enable

set qos defaultcos 1

set qos map 2q1t 2 1 cos 5

Scenario 9-1 XYZR1 Configuration

hostname XYZR1

!

enable secret cisco

!

clock timezone NZT 12

!

ip dhcp excluded-address 192.168.1.1 192.168.1.99

ip dhcp pool QOSLAB

network 192.168.1.0 255.255.255.0

option 150 ip 192.168.1.5

default-router 192.168.1.5

!

telephony-service

ip source-address 192.168.1.5

load 7910 P004G302

max-ephones 24

max-dn 48

dialplan-pattern 1 508339.... extension-length 4

!

ephone-dn 1

number 4001

name PHONE X

ephone-dn 2

number 4002

name PHONE Y

!

ephone 1

mac-address 0007.0ea6.398d

button 1:1

ephone 2

mac-address 0007.0ea6.33da

button 1:2

!

tftp-server flash:SEPDEFAULT.cnf

tftp-server flash:P004G302.bin

!

interface ethernet0/0

no shutdown

ip address 192.168.1.5 255.255.255.0

!

line vty 0 4

password cisco