The Nook Book

ISBN-13:  9780789741196

Errata 3/8/2011

The NOOKcolor Unrooting Process

Since I wrote the book, the unrooting process has changed a bit from what I indicate on page 151. Please follow these instructions (adapted from nookdevs.com <http://nookdevs.com/> ):

Part 1: Restart and Interrupt the Starting Process Eight Times

- Turn off your NOOKcolor.

- Turn on your NOOKcolor. Do not turn away.

- When you see the "Welcome to the future of reading" screen, press and hold the power button. This interrupts the start up process. If the Android start up animation does not appear, count 1 or add 1 to your start up count. If the Android start up animation appears, the restarting count is reset to 0, and you'll have to start over again.

- Repeat the process from step 2 until you get up to eight on the restart count.

- The NOOKcolor at this time flashes its firmware and you will see a screent that reads "Installing, A new software update is being installed. This will take a few minutes." Let the process finish.

Part 2: Reset the Device

- With the NOOKcolor off, hold the Home button and the power button. The NOOKcolor starts up. Keep holding the buttons.

- You will see a screen to reset your NOOKcolor to factory settings with two options. Press Power to exit. Press Home to continue.

- Press the Home button. You will be given the two options again.

- Press the Home button.

- Your NOOKcolor erases the data, deregisters, and reboots the device.

Your NOOKcolor is no longer rooted.