Optimal Routing Design

1st Edition

Copyright © 2005 Cisco Systems, Inc.

ISBN-10: 1-58705-187-7
ISBN-13: 9-781-58705-187-6

Warning and Disclaimer

Every effort has been made to make this book as complete and as accurate as possible, but no warranty or fitness is implied. The information provided is on an "as is" basis. The author and the publisher shall have neither liability nor responsibility to any person or entity with respect to any loss or damages arising from the information contained in this book or from the use of the CD or programs accompanying it.

When reviewing corrections, always check the print number of your book. Corrections are made to printed books with each subsequent printing.

First Printing: June 2005

Corrections for all Printings

| Pg | Error | Correction |
| --- | --- | --- |
| 38 | Chapter 2, Forwarding Traffic, Last Paragraph, First Sentence Reads: Interlayer traffic is traffic that is forwarded within the network layer, whereas intralayer traffic is traffic that is forwarded between network layers. | Should read: Intralayer traffic is traffic that is forwarded within the network layer, whereas interlayer traffic is traffic that is forwarded between network layers. |
| 67 | Chapter 2, Multiple Points of Redistribution Reads: 4. Router D receives 10.1.1.0/24 as an EIGRP external and readvertises it to Router E. 5. Router E receives the route to 10.1.1.0/24 and prefers this external. Router D redistributes this route into OSPF with a cost of 5. | Should read: 4. Router E receives 10.1.1.0/24 as an EIGRP external and readvertises it to Router D. 5. Router D receives the route to 10.1.1.0/24 and prefers this external. Router E redistributes this route into OSPF with a cost of 5. |
| 70 | Chapter 2, Bullet point 5 Reads: Router G receives the redistributed route from Router F, tagged 250. Router G has a filter to block routes that are tagged 250, so it blocks this update, preventing the second possible routing loop. | Should read: Router H receives the redistributed route from Router F, tagged 250. Router h4444 has a filter to block routes that are tagged 250, so it blocks this update, preventing the second possible routing loop. |
| 166 | Chapter 4, Bullet point 3 Reads: An OSPF external route with metric Type 2, a redistributed metric of 200, and a cost to reach the ASBR of 10 through Router D. | Should read: An OSPF external route with metric Type 2, a redistributed metric of 20, and a cost to reach the ASBR of 10 through Router D. |
| 384 | Appendix A, First paragraph, 3rd sentence reads: Because the path through Router C will be two hops, and the path through Router A will be three hops, Router B would choose the path through Router A and discard the alternate path it learned through Router C. | Should read: Because the path through Router C will be three hops, the path through Router A will be two hops, Router B would choose the path through Router A and discard the alternate path it learned through Router C. |
| 389 | Appendix A, Under Figure A-4, first line Reads: Router B receives three advertisements for 10.1.1.0/24 ….. Now Router B chooses the best path (lowest metric), known in EIGRP as the //feasible distance//, to 10.1.1.0/24, ........ Note** for the calculations to come out the same, do them in the same order and use the same routing techniques. | Should read: Router B receives three advertisements for 10.1.10/24 (EIGRP uses the term //reported distance//): Through Router A with a metric of 2500096 ((10^7/1500) + 3100) * 256 Through Router C with a metric of 281600 ((10^7)/10000) + 100) * 256 Through Router D with a metric of 2500096 ((10^7)/1500) + 3100) * 256 Router B adds the metric through the interface from which it receives the advertisements and now has the following paths: Through Router A with a metric of 2756096 ((10^7/1500) + 4100) * 256 Through Router C with a metric of 1988096 ((10^7/1500) + 1100) * 256 Through Router D with a metric of 2756096 ((10^7/1500) + 4100) * 256 Now Router B chooses the best path (lowest metric), known in EIGRP as the //feasible distance//, to 10.1.1.0/24, ........ |
| 400 thru 408 | Headers (every even page number) Reads: Chapter B: OSPF Basics of Operation | Should read: Appendix B: OSPF Basics of Operation |
| 402 | Appendix B, Third bullet point Reads: Router D would generate a type 1 LSA into area 0 with a connection to Router E, and include a connectiton to the network between Routers D and E. | Should read: Router D would generate a Type 4 LSA into area 0, including the cost to reach Router A. This type 4 LSA is generated because Router A is setting a bit in it’s router LSA (Type 1), indicating that it is an ASBR (as it is redistributing a connected route into OSPF). |

This errata sheet is intended to provide updated technical information. Spelling and grammar misprints are updated during the reprint process, but are not listed on this errata sheet.